## Slide 1: CO2 Methods of Injection

## Slide 2: TOMCO Systems | General Overview
6
CONFIDENTIAL
C H ANG I NG T H E W AY Y O U T HI NK ABO U T CO 2
50+ Years in business
Located in Loganville, Georgia (metro Atlanta) since 1970
  84,000 sq ft; 15+ acres
  Recently acquired adjacent 2.75 acres for future expansion
Capable of Manufacturing Pressure Vessels up to 120-Tons
Certifications: ASME, ASME R, KGS, CE Mark, PED, CRN, FM, DOT, National Board of US
Highly experienced Management Team
Well diversified market segmentation for products and services
CO2 Liquefaction, CO2 ReGeneration & Dry Ice Production Equipment
Extensive Field Service and Technical Support infrastructure
Loganville, GA

## Slide 3: Air Water Inc. | About
Headquartered in Osaka, Japan with
~$8.9B in Annual Sales (95% in Japan)
18,000+ Employees
A Market Leader in Japan Industrial Gas & Cryogenic Equipment with
~$2B in sales
Focus on International Growth and Acquisitions
Manufacturing Companies with Engineered Industrial Gas Products
Gas Plants & Production
Acquire, Invest, Grow & Hold

## Slide 4
Gas & Engineering
Cryogenic Equipment
AIR WATER GAS SOLUTIONS INC.
Cryogenic Freezer – CO2/LN2
-Tunnel Freezer
-Batch Freezer
-Spiral Freezer
-Tumbler
Gas Application
-Water Treatment System
-Fire Suppression System
-Dry Ice related equipment
Cryogenic Equipment
-CO2 delivery & storage
EPC
-CO2 Plants
Cryogenic Equipment – N2/H2/LNG
-Tanks & Cylinders
-Trailers
-ISO Containers
-Rail Cars
-HP Hydrogen Refuelers
-Vaporizer/VIP
Plant Engineering
-Air Separation Plant
-H2 Production/Liquefaction
-CO2 Purification/Liquefaction
Gas Production & Supply
-Plant Operation & Maintenance
-Industrial Gas Supply
(O2, N2, Ar, H2, CO2)
H2 Fuel Stations
H2 Fuel Stations and Distribution
-$50M Investment
Public hydrogen stations
Largest station operator in California serving FCEV’s

## Slide 5: TOMCO Systems | General Overview
12

## Slide 6: What is CO2? How is it made?
Carbon Dioxide is a gas at normal atmospheric temperature and pressure.
Colorless, odorless gas that is about 1.5 times denser than air.
Dissolves in water to form carbonic acid; H2CO3. Carbon dioxide gas is formed from the combination of two elements: carbon and oxygen.
CO2 is produced from the combustion of coal or hydrocarbons, the fermentation of alcohols, the production of anhydrous ammonia, by-product of other chemical processes, occur naturally in deep CO2 wells and the breathing of humans and animals.
Found in small proportions in the atmosphere, it is assimilated by plants which in turn produce oxygen.

## Slide 7: Adjusting pH | Why do we do it?
Stabilize Water Chemistry
Corrosion Control
Discharge Water (Permit)
Reduce or prevent Carbonate Scaling
Enhance chemical reaction or process
Polymers, Chlorine, Lime, Filtration, Contaminant removal

## Slide 8: Carbon Dioxide pH Control Equipment
CO2 Storage
Vaporizer
Vapor Heater
Pressure Regulator
CO2 / H2CO3 Feed Panel
Diffuser

## Slide 9: CO2 Bulk Storage
E/WTC-Style Series
  3.75 Tons – 120 Tons Capacity
C-Style Series
  3.75 Tons – 60 Tons Capacity
V-Style Series
  6 Tons – 100 Tons Capacity

## Slide 10: General Tank Layout

## Slide 11: Products | CO2 Vaporizers
Variety of Vaporizers
  Electric Pressure Build
    245 lb/hr – 2150 lb/hr
  Direct to Process
    375 lb/hr – 2250 lb/hr
  Steam
    500 lb/hr – 18,000 lb/hr
  Water
    500 lb/hr – 20,000 lb/hr

## Slide 12: Products | CO2 Vapor Heaters
Electric
  720 lb/hr to 1440 lb/hr (Wall)
  2000 lb/hr to 6000 lb/hr (Floor)
Steam
  500 lb/hr to 6,000 lb/hr

## Slide 13: Products | CO2 Feed Equipment
CO2 Gas Feed
  60% - 85% efficiency of the
  carbon dioxide
  Needs deep contact or holding basins.
  Able to reduce the pH to 7.0
Carbonic Acid (PSF)
  Minimum 95% efficiency of the carbon dioxide
  Able to reduce the pH to 5.5 – 6.0
  Can be injected in a pipe, basin, tank or shallow channel.
  Eliminates the need for deep contact or holding basins.

## Slide 14: Products | CO2 Gas Injection
Gas (CO2) + Liquid (water) reaction takes time
Requires tremendous surface area (fine bubbles)
Interference of other gases; i.e. air
Requires mixer or baffles to hold the gas down in the water
Lower efficiencies due to gas bubbles at the surface

## Slide 15: Products | Carbonic Acid Injection (PSF)
CO2 pre-reacted to form Carbonic Acid
Liquid / Liquid (Carbonic Acid / Water) Reaction
Immediate reaction (Requires less time)
Close to 100% efficiency
Higher pressure improves CO2 solubility
More effective pH control
Faster reaction time reduces scale potential.

## Slide 16: Products | CO2 Diffusers
Gas Feed
  Uses fine porous diffuser to disperse the CO2 into a deep basin.
Carbonic Acid
  Disperses Carbonic Acid into a water stream to form the chemical reaction desired. Designed to fit in any situation

## Slide 17: Products | Carbonic Acid Diffusers
Counter Current
Cross Sectional Coverage
Pressure
Efficient Mixing
Immediate Reaction
Patent # 6637731 & 6767008

## Slide 18: Typical Flow Schematic

## Slide 19: Why does TOMCO2 Use a 1:1 Ratio of Carrier Water to CO2?
At atmospheric conditions, we can dissolve 1 volume of CO2 into 1volume of water.
Soft drink companies increase that pressure to 60 psig, thereby, allowing 5x more the CO2 to be dissolved into your drink.
What happens when you open a coke can? You hear a fizz! The pressure drop that occurs causes the CO2 to off-gas due to supersaturation of the available liquid supply.
By using readily available carrier water in a 1:1 ratio of lb/hr CO2 to GPM carrier water, we adequately dissolve sufficient CO2 required for neutralization without offgassing.
While our competitor may claim that they use less carrier water than TOMCO2, they are super saturating their solution. The lack of carrier water leads to decreased efficiency when encountering a pressure drop. TOMCO2 ensures sufficient carrier water is used to maintain the CO2 in solution throughout the process.
The carrier water TOMCO2 requires is recycled through the system!

## Slide 20: Areas to Use CO2
Municipal Water Plants
  Lime Softening
  Enhanced Coagulation
  Stripping – H2S
  Corrosion Control
  Membranes including RO
  Disinfection – Sodium Hypochlorite
  Filter Backwash
  Bromate Reduction
  Arsenic Removal
  Chromium-6 Removal
  Well Rehabilitation
  Aquifer Storage & Recovery (ASR)
  Ion Exchange Odor Control
  Wastewater Discharge

## Slide 21: Other Areas
Power Industry
pH Control for Ash Ponds
pH Control for wastewater and Boiler Blow Down water.
Scale reduction of cooling water
Steel & Chemical Industry
pH Control for Wastewater, Boiler blow down water.
Textile Industry
pH Control for Wastewater.
Concrete & Mining Industry
pH Control for Wastewater.
pH Control for Storm water Run Off.
Food and Beverage Industry
Carbonation
Formation of Hypochlorous Acid For Bacteria Kill
pH Control for Wastewater.

## Slide 22: Other pH Control Methods
Liquid CO2 Feed Systems
Gas Eductor / Vacuum Feeder
Chlorinator / Solution Feeder
Carbonated Water Feeder
Mineral Acids

## Slide 23: Manufacturer’s Qualifications
Experience in CO2 and Water Treatment Systems
Over 1,700 systems installed
Active member of CGA
Engineering Capability
Optimized pH control and CO2 utilization
Total System Responsibility
ASME Pressure Vessel shop
Service Capability
Made in the USA- Loganville, GA

## Slide 24
Water Technologies
Camila Cando
Sales Application Engineer
ccando@tomcosystems.com
(c): 678-326-347
www.tomcosystems.com